## Slide 1: benchmarking STREAM
Stefano Cozzini
AreaSciencePark

## Slide 2: Resource to benchmark
CPU/GPU
Computational speed
Memory Hierarchy
(bandwith/latency)
Node Interconnect

## Slide 3: Stream benchmark
Created in 1991
Intended to be an oversimplified representation of low-computing intensity and long vector operations
Realistic baseline for memory bandwidth on HPC system
Widely used, more 1100 results in the database
Hosted at www.cs.virginia.edu/stream
Compilation and execution trivial
Warning: reported and actual BW numbers may differ..

## Slide 4: Stream
Four kernels, separately timed:
N chosen to make each array >> cache size
Repeated several times, first iteration ignored
Min/Max/Avg reported and the best time used to compute Bandwidth
TYPE | OPERATION | BYTE/cycle | FLOPS/cycle
COPY | A(:) = C(:) | 16 | 0
SCALE | A(:) = s * C(:) | 16 | 1
ADD | A(:) = B(:) + C(:) | 24 | 1
TRIAD | A(:) = B(:) + s * C(:) | 24 | 2

## Slide 5: Stream: which kind of performance can we expect ?
Let us take a look how memory is organized on modern Intel CPU on ORFEO

## Slide 6: Memory layout on skylakeX processors
Picture from : Intel Xeon Scalable Family Balanced Memory Configurations (lenovopress.com)

## Slide 7: Memory should be balanced !
Three rules:
  All populated memory channels should have the same total memory capacity
  All memory controllers on a processor socket should have the same configuration of DIMMs
  All processor sockets on the same physical server should have the same configuration of DIMMs

## Slide 8: ORFEO Intel : RAM
NODE TYPE | processor | # Channels | Max speed | Memory types
THIN | Xeon(R) Gold 6126 | 6 | 2666MT/sec | DDR4-2666
FAT | Xeon(R) Gold 6154 | 6 | 2666MT/sec | DDR4-2666
GPU | Xeon(R) Gold 6226 | 4 | 2933MT/sec | DDR4-2933
see https://www.intel.com/content/www/us/en/products/processors/xeon/scalable/gold-processors.html
𝑏𝑝𝑒𝑎𝑘= # 𝐶ℎ𝑎𝑛𝑛𝑒𝑙𝑠 × 𝑓𝑀𝐸𝑀 × 8𝐵/𝑐𝑦𝑐𝑙𝑒

## Slide 9: Memory layout on ORFEO thin node
RAM=768 GB 12 LRDIMM of 64 GB each
12 on each single processor

## Slide 10: Memory layout on ORFEO fat node
RAM=1536GB 24 LRDIMM of 64 GB each
12 on each single processor

## Slide 11: Memory layout on ORFEO gpu node
RAM=256 GB 8 LRDIMM of 32GB each
4 on each single processor

## Slide 12: ORFEO Intel nodes: peak performance
NODE TYPE | processor | # Channels | # socket | Memory types
THIN | Xeon(R) Gold 6126 | 6 | 2 | 6x2666x8x2 =~ 256GB/sec
FAT | Xeon(R) Gold 6154 | 6 | 2 | 6x2666x8x2 =~ 256GB/sec
GPU | Xeon(R) Gold 6226 | 4 | 2 | 4x2933x8x2 =~ 188GB/sec

## Slide 13: NUMA performance problem
NUma:
  Whole memory is transparently accessible
  But physically distributed with different latency and bandwidth
  => potential contention
How to we make sure that memory access is always as “local” and “distribute” as possible ?

## Slide 14: Thread Affinity and Data Locality
Affinity
  Process Affinity: bind processes (MPI tasks, etc.) to CPUs
  Thread Affinity: further binding threads to CPUs that are allocated to their parent process
Data Locality
  Memory Locality: allocate memory as close as possible to the core on which the task that requested the memory is running
  Cache Locality: use data in cache as much as possible
Correct process, thread and memory affinity is the basis for getting optimal performance.

## Slide 15: Thread placement - numactl
numactl is a command of the operating system providing much focused on the NUMA features of a system.
numactl understands which processors form a NUMA node and how threads need to be grouped together
Important options:
--membind <n>: place pages on NUMA node <n>
--cpunodebind <n>: pin threads to node <n>
--interleave <nodes>: put the pages round-robin on <nodes>
Example:
numactl --cpunodebind=0 --membind=0,1 ./a.out
This puts memory on nodes 0 and 1, but threads only on node 0.

## Slide 16: STREAM performance on 1 socket (thin node)
Chart: STREAM performance on 1 socket
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12
socket 0/1 | 8485.4 | 16309.9 | 22951 | 29575.3 | 33471.3 | 34306.3 | 34264.6 | 34382.2 | 34295.7 | 34320.8 | 34270.6 | 34137.2
socket 0/0 | 11759.4 | 22721.4 | 32836.3 | 43982.7 | 52356.3 | 56962.2 | 60761.6 | 64948.8 | 66890.5 | 69284.5 | 70168.6 | 70254.9
socket1/0 | 8498.4 | 16355.4 | 23067.8 | 29563.7 | 33499.2 | 34310.3 | 34175.3 | 34348.7 | 34259.6 | 34326.9 | 34240.7 | 33783.9
socket1/1 | 11768.1 | 22687 | 32861.8 | 44147.9 | 52243.6 | 56843.1 | 60696.6 | 64912.7 | 66852.6 | 69348.5 | 70212.6 | 69655

## Slide 17: Stream in action:
Naïve way:
Pinning processor: likwid-pin –c N:0-23 ./stream.x

## Slide 18: Stream on ORFEO Epyc nodes
See the the excellent tutorial prepared by Niccolo on the github repo